## Slide 1: Internet from a MSX computer
Néstor Soriano (Konamiman)
http://www.konamiman.com
Notes: Thanks for coming
Who am I
What I'm going to do (first, presentation; then, practical demonstration)

## Slide 2: The pioneers: UZIX
Developed by Adriano C. R. da Cunha
Notes: My software is not the first one that allows connecting a MSX to internet
Uzix, Unix implementation for MSX by A. Cunha.
About 1999
Web browser using a proxy server that simplifies HTML and images

## Slide 3: The InterNestor saga
2002: InterNestor Suite
  Final project of telecommunication engineering
  TCP/IP stack with modular design (exchangeable modules for hardware access, link level, network level and transport level)
  Implemented modules: RS232, PPP, IP, TCP
  64K for code + memory manager for data
  Requires MSX with 256K RAM
  Excessively slow
Notes: It was 2001 and I was studying telecommunications engineering
I had to choose a project: internet for MSX
OSI model = Open Systems Interconnection

## Slide 5: The InterNestor saga
2002: InterNestor Suite
2003: InterNestor Lite
  Goal: reduce memory consumption and improve performance
  16K for code + 16K for data
  Targeting the same hardware as INS (RS232 + PPP)
  API incompatible with INS

## Slide 6: 2004: ObsoNET
By Daniel Berdugo (hardware) & Néstor Soriano (BIOS)
Notes: Handmade, about 30 units produced
I developed the BIOS (basic routines for hardware access, packet input/output, network state checking)
INL worked only with RS232

## Slide 7: The InterNestor saga
2002: InterNestor Suite
2003: InterNestor Lite
2004: InterNestor Lite for ObsoNET
  Built upon the code of INL of RS232
  API compatible “enough” with INL for RS232 (compatible at the network and transport levels)

## Slide 8: 2007: UNAPI specification
  Standard to define APIs for MSX
  Defines a group of rules that APIs must follow:
    API identifier + implementation name
    One single entry point for all routines
    Defines a procedure for discovering the installed API implementations
  An API for Ethernet cards is defined initially
Notes: I thought: what if someone else builds an ethernet card for MSX?
I'll create a standard for Ethernet APIs
But then I thought: better a standard for APIs

## Slide 9: The InterNestor saga
2002: InterNestor Suite
2003: InterNestor Lite
2004: InterNestor Lite para ObsoNET
2007: InterNestor Lite for Ethernet UNAPI
  Replaces INL for ObsoNET
  Same API as INL for ObsoNET
  ObsoNET BIOS 1.1 implements Ethernet UNAPI

## Slide 10: 2009: DenYoNet
By Dennis Koller (DD) & Jos van den Biggelaar (Yobi)
Produced by Sunrise for MSX

## Slide 11: The InterNestor saga
2002: InterNestor Suite
2003: InterNestor Lite
2004: InterNestor Lite para ObsoNET
2007: InterNestor Lite para Ethernet UNAPI
2010: TCP/IP UNAPI specification
+
InterNestor Lite 2
  Two versions: for RS232 and for Ethernet UNAPI
  Replaces INL 1
  API incompatible with INL 1
  Implements the API for TCP/IP UNAPI

## Slide 12
Too many API changes!!
Sorry!

## Slide 13: 2009: DenYoNet
Two BIOS available:
  BIOS compatible with Ethernet UNAPI
    The W5100 is used as a simple Ethernet controller
    To be used with InterNestor Lite 2 for Ethernet UNAPI
  BIOS compatible with TCP/IP UNAPI (under development)
    Uses the TCP/IP capabilities of the W5100
    To be used directly, without InterNestor
In both cases the same client applications are used (they use the first available TCP/IP UNAPI implementation)

## Slide 14
INL for RS232
RS232 port
INL for Ethernet
ObsoNET
DenYoNet (BIOS TCP/IP)
API TCP/IP
API Ethernet
FTP, Telnet, e-mail...
DenYoNet (BIOS Ethernet)

## Slide 15: How does INL work?
VDP MSX
50/60 Hz
Update timers
  Update state / Send one packet (DNS, DHCP)
Receive one packet
  Update state / Send reply
Process one TCP connection
  Send one segment
There’s no multitask!
Notes: There's no multitask in MSX (Z80)
The MSX VDP generates interrupts with the same frequency as the screen refresh
INL captures the interrupt
The TCP connections are processed in each interrupt
Seen from far away, in a moonless night, and with dense fog, it remotely looks like cooperative multitasking

## Slide 16: INL features What does fit in 16K+16K?
  TCP: 4 connections (1K in + 1K out)
  UDP: 3 connections (buffer for 1 packet)
  Sends/receives PINGs (no data is stored)
  DNS: Only resolves 1 name at the same time
  DHCP for local IP, remote IP, gateway IP, network mask
  ARP: table with 32 entries (dynamic and static)
  Routing table: 16 entries

## Slide 17: INL limitations What does NOT fit in 16K+16K?
  NO datagrams >576 bytes
  NO ICMP (except PING)
  NO TIME-WAIT state for TCP
  NO loopback address (127.x.x.x)
  NO IP fragmentation
  NO DNS cache
  NO >9600 bauds (Z80) / >19200 bauds (R800)
  Max theoretical speed: aprox. 30KByte/sec

## Slide 18: And now… let’s get some action!